Horton Local Oscillator – discussion paper – Phil Harman VK6APH

This design is  based on an original suggestion by Phil Covington, N8VB.

Further thoughts on the Horton LO.  This time I’ve tried to restrict the tuning range of the uW VCO since that will reduce it’s phase noise.  Here is the block diagram

In this case the  reference frequency (Ref) into the PFD is fixed at 800kHz.  The divide by N is an NB7N017M from ON Semiconductors  which is an ECL 3.5GHz input 8 bit divider, see

http://www.onsemi.com/pub/Collateral/NB7N017M.PDF

By selection of  M and N we can cover 1 to  30MHz in <10kHz steps as per the following table.  Delta I/Q shows the frequency change as a result of increasing M by 1.

| I and Q |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Freq (MHz) | Fo | N | M | F (MHz) | Ref(MHz) | M + 1 | Delta I/Q (MHz) |
| 1 | 4 | 600 | 3000 | 2400 | 0.8 | 3001 | 1.0003 |
| 2 | 8 | 300 | 3000 | 2400 | 0.8 | 3001 | 2.0007 |
| 3 | 12 | 200 | 3000 | 2400 | 0.8 | 3001 | 3.0010 |
| 4 | 16 | 150 | 3000 | 2400 | 0.8 | 3001 | 4.0013 |
| 5 | 20 | 120 | 3000 | 2400 | 0.8 | 3001 | 5.0017 |
| 6 | 24 | 100 | 3000 | 2400 | 0.8 | 3001 | 6.0020 |
| 7 | 28 | 86 | 3010 | 2408 | 0.8 | 3011 | 7.0023 |
| 8 | 32 | 75 | 3000 | 2400 | 0.8 | 3001 | 8.0027 |
| 9 | 36 | 67 | 3015 | 2412 | 0.8 | 3016 | 9.0030 |
| 10 | 40 | 60 | 3000 | 2400 | 0.8 | 3001 | 10.0033 |
| 11 | 44 | 55 | 3025 | 2420 | 0.8 | 3026 | 11.0036 |
| 12 | 48 | 50 | 3000 | 2400 | 0.8 | 3001 | 12.0040 |
| 13 | 52 | 47 | 3055 | 2444 | 0.8 | 3056 | 13.0043 |
| 14 | 56 | 43 | 3010 | 2408 | 0.8 | 3011 | 14.0047 |
| 15 | 60 | 40 | 3000 | 2400 | 0.8 | 3001 | 15.0050 |
| 16 | 64 | 38 | 3040 | 2432 | 0.8 | 3041 | 16.0053 |
| 17 | 68 | 36 | 3060 | 2448 | 0.8 | 3061 | 17.0056 |
| 18 | 72 | 34 | 3060 | 2448 | 0.8 | 3061 | 18.0059 |
| 19 | 76 | 32 | 3040 | 2432 | 0.8 | 3041 | 19.0063 |
| 20 | 80 | 30 | 3000 | 2400 | 0.8 | 3001 | 20.0067 |
| 21 | 84 | 29 | 3045 | 2436 | 0.8 | 3046 | 21.0069 |
| 22 | 88 | 28 | 3080 | 2464 | 0.8 | 3081 | 22.0071 |
| 23 | 92 | 27 | 3105 | 2484 | 0.8 | 3106 | 23.0074 |
| 24 | 96 | 25 | 3000 | 2400 | 0.8 | 3001 | 24.0080 |
| 25 | 100 | 24 | 3000 | 2400 | 0.8 | 3001 | 25.0083 |
| 26 | 104 | 24 | 3120 | 2496 | 0.8 | 3121 | 26.0083 |
| 27 | 108 | 23 | 3105 | 2484 | 0.8 | 3106 | 27.0087 |
| 28 | 112 | 22 | 3080 | 2464 | 0.8 | 3081 | 28.0091 |
| 29 | 116 | 21 | 3045 | 2436 | 0.8 | 3046 | 29.0095 |
| 30 | 120 | 20 | 3000 | 2400 | 0.8 | 3001 | 30.0100 |

I have done a worst case VCO frequency swing analysis and this indicates the VCO needs to tune from 2400MHz to ~2520MHz, a 120MHz swing.

At worst case we divide the VCO by 80 which gives us a theoretical 38dB reduction in phase noise.

There are a couple of things to note:

- In the 1-3MHz band the N divider ratio is > 256. I guess we could always divide by other than 4 at I & Q to overcome this.

- We are going to need to vary N within a 1MHz band at some  frequencies in order to keep the VCO within the above range.  The math to calculate each frequency step will be ‘interesting’ but nothing we can’t handle.

Comments and feedback welcome.

Phil Harman VK6APH 8th July 2006

© All rights reserved